## 3D Industries Australia - Joey 3
The Joey is a medium format 3D printer, on-loan from 3D Industries. It has proved reliable and is used when a larger build platform is required.
Below is the information from 3D Industries:

The Joey has a frame measuring 500 mm wide by 500 mm deep and 500 mm tall. It has a standard build platform size of 300 mm by 300 mm. / Objects can be built up to a height of 190 mm. / The Joey Wombat and Possum utilizes a CoreXY mechanism to move the extruder carriage in the X and Y axis at the top of the frame. The heated build platform descends as each layer is printed. / The power supply is contained within the frame and the filament spool holder can be mounted in different positions. / The printers are controlled by means of an LCD screen controller - no connection to a PC is required. Objects to be printed are stored on an SD card in gcode format. / The hot end extruder used is the latest 3D Industries Aluhotend and an automatic gap sensor is included to ensure the correct clearance between the nozzle and the bed.

### Config
The Joey model config file has:
- 0.3 layer height - 2 perimeters
- infill rectilinear at 45 degrees and 70% density
- 5 circle skirt 1 layer high
- No support material
- Latest advanced settings
- PLA filament (nozzle) temp of 260C and bed temp of 60C
- fans always on
To access the cloud based support site use this link:
https://drive.google.com/open?id=0B9NxCU9Ht-wgenhvU2kwd1NmWVk
To access the software download the required files or directory to the local system.
### SLicer Config file
config-pla-normal.ini.zip
### Manuals from the 3DI Google Drive
commissioning_the_printer_v.1.pdf
flexi_filament_printing_v1.1.pdf
flashforge_bed_material_v1.0.pdf
1-read-me-first.pdf
bed_levelling_procedure_v1.0.pdf
software_installation_v1.0.pdf
hot_end_changing_v1.0.pdf
hot_end_changing_v1.0.pdf