# CNC Tooling
Standard Vcarve settings used in the Fabrication Lab including The Edge CNC tool database
# Router Tooling
## Router Bits
### End Mills
#### Small Compression
#### Large Compression
#### Straight Cut
#### Up Cut
#### Down Cut
### Drill Bits
## Drag Knife
- Fits in a 1/4in router collet (7mm)
- Enables you to cut thicker materials
- Maximum cutting depth: 1/4 in. (6.3mm)
- Minimum cut radius in materials thinner than 1/8 in. (3.1 mm): 1/8 .in (3.1mm)
- Minimum cut radius in materials over 1/8 in. (3.1mm) thick: equals material thickness
- Offset 4mm
#### Creaser
Creasing Attachment
Fits on all Donek Tools Drag Knives (D2 or D4 recommended) Can be used to Crease cardboard and foam Can be used with a 28mm Olfa (TM) or Fiskars (TM) rotary cutting wheel Tool Offset (20.3mm)