## Slide 2
Arduino 102
Coding Concepts

## Slide 3
Acknowledgement of country
We acknowledge Aboriginal and Torres Strait Islander peoples and their continuing connection to land and as custodians of stories for millennia. We respectfully acknowledge the land on which we all meet today, and pay our respects to elders past, present and emerging.

## Slide 4
What we’ll work on today:
The structure of Arduino code
Common programming constructs
The value of pseudocode
Make your NeoPixel ring do what you want!
By the end of our session you’ll have full control of your LED ring.
Workshop Overview

## Slide 5
TOOLS
1x Arduino Uno
1x USB cable
1x LED ring
1x breadboard
10x breadboard jumper cables

## Slide 6
Health & Safety
We are exposing ourselves to a low voltage today so when we’re dealing with the live cables and the breadboard, be mindful of the connections you’re making with the cables.

## Slide 7: What is a microcontroller?
A microcontroller (or MCU for microcontroller unit) is a small computer on a single integrated circuit.
It has:
  one or more CPUs (processor cores)
  memory
  programmable input/output peripherals
It can interact with
    digital signals
    analogue signals

## Slide 8: Why use a microcontroller?
They’re compact, so they can fit inside ‘things’ to make them extra useful.
They’re low power, so they can run for a long time off a battery.
They’re robust, so they can continue to function in most environments.

## Slide 9: Why Arduino?
Arduino is an open source hardware and software project.
The hardware is based on the Amtel 8-bit AVR MCU
Great IDE with a simple C-like programming language.
Open source means it has a huge range of compatible devices, guides, and sketches.
A strong community means
“Someone, Somewhere has solved the problem”
we can run this workshop using and adapting existing resources.

## Slide 10: Coding Concepts: File Structure
Every Arduino 'sketch' has the same overall structure:
A setup function, that runs once on start up.
And a main loop, that repeats until the end of time.

## Slide 11: Coding Concepts: Variables
Variables are a tool we use a lot in coding, no matter the language or application.
Variables are like little labelled containers that we can store things inside. We basically nickname a corner of memory so we can access or update it quickly during runtime.
Each variable has a type, a name and a value, which looks like this:
int buttonPin = 13;
We can 'access' the value by using the label 'buttonPin', meaning it gets substituted anywhere we put the variable name.
So, we write this: pinMode(buttonPin, INPUT);
And it gets translated into this: pinMode(13, INPUT);
Notes: For more: https://docs.arduino.cc/learn/programming/variables/

## Slide 12: Coding Concepts: Functions
Functions collect a series of repeatable, low-level steps under a convenient name so we can run those steps quickly and easily.
Imagine we are programming a little robot and we want it to be able to turn right because it only knows how to turn left.
We might realise that three left turns equals one right turn. So we'd create a TurnRight() function and give it a set of steps:
Step 1: TurnLeft()
Step 2: TurnLeft()
Step 3: TurnLeft()
Notes: https://docs.arduino.cc/learn/programming/functions/

## Slide 13
Anatomy of a Function

## Slide 14: Coding Concepts: Pseudocode
One of the most important skills when coding is being able to break down your big goal into the tiniest steps possible, because those steps are what you will turn into code.
A great practice to get into is going through and writing out – in conversational rather than technical syntax – all the steps your code will need to take to achieve its task.
Then you can write the code to do it.
This little step helps with planning, debugging, problem solving and readability.

## Slide 15: Coding Concepts: Pseudocode
BEGIN Arduino Program
// Setup function (runs once when the Arduino starts)
FUNCTION setup():
SET LED_PIN as an OUTPUT
END FUNCTION
// Main loop function (runs repeatedly after setup)
FUNCTION loop():
TURN LED_PIN HIGH (turn LED on)
WAIT for 1000 milliseconds
TURN LED_PIN LOW (turn LED off)
WAIT for 1000 milliseconds
END FUNCTION
END Arduino Program

## Slide 16: Coding Concepts: Loops
Loops are useful everywhere, all the time.
There are different types of loops (for loops, while loops, do-while loops), but they all share the same big idea: Execute a block of code, over and over again, until some condition is met.
The different 'types' of loop relate to what kind of condition we want, and at which points in time we check to see if it's been met.
The two most common loops are:
"For every item in this sequence (i.e. list), run this loop"
"While this thing is true, run this loop"
Notes: https://docs.arduino.cc/micropython/basics/loops/

## Slide 17: Coding Concepts: For Loops
for (initialization; condition; increment/decrement) {
Code to be executed repeatedly
}
for (int i = 0; i < 5; i++) {
Serial.print(i);
}
Notes: https://docs.arduino.cc/micropython/basics/loops/

## Slide 18: Coding Concepts: While Loops
while (true or false condition) {
Code to be executed repeatedly
}
int var = 200;
while (var < 200){
var++;
}
Notes: https://docs.arduino.cc/language-reference/en/structure/control-structure/while/

## Slide 19: Coding concepts: Conditional branches
We control the flow of code intelligently using 'if' statements.
You do this in your daily conversations all the time: "If they have salami, get that. Otherwise, I'll have ham."
If (salami) {
Get salami;
} else {
Get ham;
}
Notes: https://docs.arduino.cc/language-reference/en/structure/control-structure/if/

## Slide 20: Coding Concepts: Doing > Discussing
The best way to understand these ideas is to see them in action in other people's code, and to use them in our own code.
So, let's do that! We will dissect a sketch and then work on some challenges.
Head over to this page and look at the code example:
https://dropbearlabs.io/workshops/arduino102/
Notes: https://dropbearlabs.io/instructor/arduino102/

## Slide 21
THANKS FOR ATTENDING
Please complete our survey that will be sent out via Eventbrite.
Tag us on socials @statelibraryqld
Contact us on appliedcreativity@slq.qld.gov.au