## Slide 1
1. MODE SELECT.
Choose how motor will operate.
For positioning:
On for degrees
On for rotations
is recommended.
When “ON” mode is selected, BOTH motors will keep running until another block tells them to turn “OFF”!
STEERING Motor Block
Used to run TWO Large motors at the same time for STEERING.
6. SELECT MOTOR PORTS
Selects which brick ports the motors are connected to.
Two ports need to be selected as there are two motors.
Any combination of A, B, C or D
2. SET AMOUNT OF TURN.
Enter any number from -100 to 100 using slider or keyboard.
(keyboard is easier)
Motor ports will make a difference to turn direction
“0” = straight ahead
“100” = Hard right turn
“-100” = Hard left turn
4. SET the number of rotations, degrees or time period (secs) for the motors to run.
This setting is dependent on the MODE selected & the one setting applies to BOTH motors.
Use keyboard to enter data.
Decimals can be used here (eg. 1.85).
5. BRAKES
Tick = ON
On is recommended.
Turns motor OFF
Motor keeps running
3. SET SPEED OF TURN.
Enter any number from
-100 to 100 using slider or keyboard.
(keyboard is easier)
“0” = stopped
“100” = full speed fwd
“-100” = full speed rev.