## Slide 1
The WAIT block can also be used to pause a program while it “waits” for a sensor value to be reached.
This is done by clicking on the “mode” button , selecting the desired sensor to be monitored (Colour in this case) & then selecting the type of change you’d like the WAIT block to look for.
WAIT Block (Colour Sensor)
Using WAIT block to read a colour sensor (PART 1)
1. Click on the “mode” button.
2. Select the sensor to be monitored.
In this case, “colour sensor” has been selected.
3. Select what change you wish the sensor to detect.
Compare = compare what the sensor detects against a value that you select or nominate.
Change = “WAIT” until any change in sensor value has been detected.
4. Select what “function” of the sensor you wish the sensor to monitor.
Some sensors are able to detect more than one thing (function).
The colour sensor can detect three things:
Colour – Detects a specific colour (red, blue, green, etc.)
Reflected light intensity – Detects the amount of light reflected back off the mat.
Ambient light intensity – Detects the level of ambient light in front of the sensor.

## Slide 2
In the sequence below, the “wait” block has been set to “colour compare”. It will “compare” the colour the sensor sees with the colour you’ve selected.
When the sensor “sees” a colour that matches the one you’ve selected, it will allow the sequence to move to the next block.
The colour selection drop down box has been opened by clicking on the second selection box .
Only the number will be shown once a colour has been selected.
In this sequence, the robot will move forward (TANK block simply turned ON) & the WAIT block will pause the sequence until the colour sensor sees RED (5).
The robot then stops because the next block is a TANK motor block with the STOP function.
NOTE: When using the WAIT block like this, ensure a block is used after the WAIT block to stop whatever function was turned on before it.
WAIT Block (Colour Sensor)
Using WAIT block to read a colour sensor (PART 2)
Select the colour to be detected.
In this case, RED(5)has been selected.
Note that TANK block has been set to ON.
This makes both motors turn continuously & they won’t turn off until another TANK block with motor function OFF is used.
Note that this TANK block has been set to OFF.
This stops the motors after the WAIT block sees the colour RED(5).
If this block wasn’t used, the motors would keep turning.
Make sure correct ports are selected!