## Slide 1
3D Printer Induction
Password on the computer is
edgeuser
Sign up for a Tinkercad account
Tinkercad.com
Enroll in the Learning Management Sytem for the induction
Inductions.slq.qld.gov.au

## Slide 3
3D Printer Induction
The Edge

## Slide 4
Acknowledgement of country
We acknowledge Aboriginal and Torres Strait Islander peoples and their continuing connection to land and as custodians of stories for millennia. We respectfully acknowledge the land on which we all meet today, and pay our respects to elders past, present and emerging.

## Slide 5
INDUCTION SUMMARY
Using the State Library 3D printers, you can turn a digital 3D model into a plastic object.
In this induction you will learn the basics of 3D modelling with Tinkercad and how to print your own model, including how to load it into the printer and cleaning up the product.
Once you've completed the induction you can book and use the State Library of Queensland’s 3D Printers at The Edge during Open lab.
Open Lab sessions are a chance to meet up with like-minded makers and tinkerers at The Edge with facilitators to support your creative needs in the space. Bookings are required to use the equipment and you will be able to book with your SLQ account once you have completed the relevant induction.
Wednesday 1.30pm – 8pm
Thursday 1.30pm – 8pm
Saturday 12pm – 5pm
For more info and to book, head to https://www.slq.qld.gov.au/visit/spaces/edge

## Slide 6
EQUIPMENT OVERVIEW
What is a 3D PRINTER?
Allows for 3D printing which is the construction of a three-dimensional object. It does this through material been deposited, joined or solidified under computer control.
The Edge has 5 Prusa model i3 MK3s+ printers, which are the successor to Original Prusa i3 MK3 and feature hardware and software upgrades offering improved reliability and ease of use.

## Slide 7
MACHINE OVERVIEW

## Slide 8
Getting Started
Make a 3D printer booking.
Set up design file or if already done, import your model into PrusaSlicer.
Staff members can make recommendations regarding part orientation, support placement, and layer height.
When ready to print grab a 3D printer form and ask an Open lab staff member to approve your job!

## Slide 9
Health & Safety
Electricity​
Fire​
Respiratory​
Crush injury
Isopropyl (eyes/breathing/flammable)
Check the safe operating procedures regularly and ask a staff member for help if you have any problems or concerns.

## Slide 10
Designing for 3D Printer
Fusion 360
Pros
Powerful professional CAD, CAM, CAE software
Lots of good tutorials online
Great for designing close tolerance mechanical parts
Free hobbyist licence available
Cons
A lot to get your head around when starting out
Full version relatively expensive (but not as expensive as others)

## Slide 11
Designing for 3D Printer
Meshmixer
Pros
Free
Great software for sculpting 3D
Good for repairing models made in other programs
Cons
Probably want to try something more intuitive first to get your head around the concepts

## Slide 12
Designing for 3D Printer
Blender
Pros
Free and open source
Great software for all types of 3D modelling and animation
Lots of tutorials and guides online
Cons
Probably want to try a simpler software first to get your head around the concept of 3D design

## Slide 13
Designing for 3D Printer
TinkerCAD
Pros
Free
Great intuitive software for getting started
Browser based
Cons
Experienced designers might get frustrated with the lack of features

## Slide 14
TinkerCAD
Let's have a go!
Head to the internet and navigate to TinkerCAD.com
Create a free account using an email address

## Slide 15
The Interface

## Slide 16
Navigating the 3-dimensional space
Moving around ​
Zoom in and out using the scroll wheel​
​
Pan & Tilt​
Right click and drag to change the aspect of your view or​
Click and drag the Cube device to rotate you view angle​
If you get lost click the home icon and it will take you back to the default view​
​

## Slide 17
Moving and manipulating shapes
Select
Using the left click (hold shift select multiple objects)
Or left click and drag a selection box around multiple objects
Resizing
Left click and drag the black or white handles to resize your shapes
Hold the SHIFT key to constrain proportions
Left click and drag the black cone to change the elevation of the shape in relation to the work plane
Moving
You can nudge a selected object around the x & y axes with the arrow keys
Rotate
Left click and drag the curly one of the 3 arrows to rotate an object, you can also type in an angle once it is highlighted.
Ruler
Drag the ruler out onto the workplace to resize or arrange shapes using typed in dimensions

## Slide 18
Moving and manipulating shapes
Select
Using the left click (hold shift select multiple objects)
Or left click and drag a selection box around multiple objects
Resizing
Left click and drag the black or white handles to resize your shapes
Hold the SHIFT key to constrain proportions
Left click and drag the black cone to change the elevation of the shape in relation to the work plane
Moving
You can nudge a selected object around the x & y axes with the arrow keys
Rotate
Left click and drag the curly one of the 3 arrows to rotate an object, you can also type in an angle once it is highlighted.
Ruler
Drag the ruler out onto the workplace to resize or arrange shapes using typed in dimensions

## Slide 19
Make a complex shape
Grouping solids and holes​
You can make complex shapes by combining and subtracting the primitive (basic) shapes using the group tool.​
Select the objects you want to combine​
And then hit the group button

## Slide 20
Exporting
Hit the export button and select STL
Save to your desired folder
Open file up in PrusaSlicer using one of our facility computers. The software will be configured correctly on our computers.

## Slide 21
What is Slicing?
The act of converting a 3D model into a set of instructions for 3D printers is called Slicing. It is the intermediate and most important step in the process of 3D printing and where The Edge staff will need to check your settings.
These are some of the main types of settings that can be controlled in a slicer software -
Print Settings: quality and speed.
Filament Settings: type of filament etc.
Printer settings: the model of printer etc.
Supports: added parts that support overhanging or bridge structures when printing.
Infill: the internal structure (density/fullness) of a 3D printed part.
3D Model
(STL file)
Slicing
(G-code file)
3D Printer

## Slide 22
Slicing with PrusaSlicer
When choosing your print settings, you need to weigh up some priorities
Does it need to be a quick print?
Or do you have time for high quality outcome?
What percentage infill do you need?
Do you need to print support?
How much filament will this use?
Would it be more time or material efficient to cut up your model?
Or maybe reorienting it will save time, plastic, support and or clean up?

## Slide 23
Further info on Supports
3D printers work by layering plastic to create a 3D object. Each new layer must be supported by the one beneath it. If part of your model starts in mid-air and is not supported by anything below, you need to add an additional support structure to ensure a successful print.
Consider if you able to alter the orientation of the model or split into multiple parts to reduce overhangs and the amount of supports generated.
PrusaSlicer can both detect areas that need supports and generate them in these places automatically.
The Paint On support option also works great to manually choose the places you want to add supports to.
Source Jakub Kočí

## Slide 24
Further info on Infill
There are a few factors when choosing an infill pattern, listed below, and you can read up on these more on the Prusa website.
Prints (even mechanical parts) rarely benefit from infill over 20%, as uneven cooling can occur on more complex infill which leads to distortions and delamination.
Print speed: How quickly can the pattern be printed?
Density: How much filament is used to create the pattern?
Visuals: How does the pattern look when using transparent filament? How does it look if the model is exposed?
Support for top layers: How well will the top layer of a print be supported?
Flexibility: How flexible will the print be with the chosen infill pattern?
Filling: How suitable is the pattern for filling with resins or other substances? This is especially important for parts that may be used as molds for casting.
Source Jakub Kočí

## Slide 25
Slicing with PrusaSlicer
Open the PrusaSlicer application. If you see the pop-up 'Configuration Update' is available, click to install the update before proceeding further.
Use the Add button to import your model/s into PrusaSlicer.
Delete /Delete All buttons to remove models.
Use Move, scale, rotate, Place on Face and cut tools to prepare the model to printing in the most efficient/effective orientation.

## Slide 26
Slicing with PrusaSlicer
Print Settings
Select a Quality / Speed setting for your print, the higher the quality, the longer the print will take.
Select the filament that corresponds with the one on the printer (check the machine before you slice).
Select a Supports setting
Select an Infill percentage

## Slide 27
Slicing with PrusaSlicer
Click Slice to slice the model into layers in the Z axis and select layers preview to view infill land
Check the Sliced Info for the cost (amount of filament used) and how long it's going to take to print.
If you are happy with the time and settings, ask a staff member to check over and fill out the print form.
Generate and export G-Code to the SD Card by clicking the Export G-Code button.

## Slide 28
Setting up the printer
STEP BY STEP
After a staff member has approved your slicing, you can head to the 3D printer you have booked to start your 3D print.
Turn on the 3D printer (switch located on the back of the Prusa machines)
Ensure the printer is set up with the correct filament and build plate.
Switch on the extractor under the 3D printer. Each extractor serves 2 printer enclosures. Make sure BOTH the extraction and return air blast gates serving the printer you are using are open. If there is no job on the 2nd printer, ensure the blast gates serving its enclosure are closed.
Insert your media (SD card for Mk3s+ or USB thumb drive for the Mk4) into the printer.
Navigate to the file on your media by turning the knob on the screen and selecting the correct G-Code file you have prepared. Select by pushing the button. The printer extruder and bed will start heating up. Your print will start when the target temperatures are attained.
Monitor the start of the print to make sure it begins with no issues; you can then leave it to print.

## Slide 29
Common print failures
Birds nest (filament non-adhesion)​
X and/or Y-axis shift (belt or stepper motor errors)​
Print wholly or partially detaches from build plate​
Blocked nozzle ​
G-code encoding error​
Thermal anomaly or runaway (hot end or bed)​
Head impact

## Slide 30
Troubleshooting
Something is weird or going wrong? ​
First reaction should aways be ​pause the job
Remember you can always ask a staff member for help!
The filament spool doesn’t unwind?
Check spool mounting and rotation
Ensure filament on spool is able to unwind without binding
The machine announces an error?
Refer to the manual for error code explanations
Check for temperature, connection, or SD card issues

## Slide 31
Filament birds nest forms
Clean clogged nozzle (staff only)
Ensure smooth filament path
Calibrate extruder and temperature settings (staff only)
The spool runs out of filament or the filament breaks?
Monitor spool and replace before empty (staff only)
Replace filament with another spool known to be dry (staff only)
The print wholly or partially detaches from the build plate?
Ensure correct build plate for specific filament type is being used.
Ensure a clean and level build plate
Adjust first layer Z height
The printer shifts in the x and/or Y axis?
Tighten belts and pulleys (staff only)
Ensure a stable, clear printing environment
Verify correct print file generation
Troubleshooting
See staff for support with any issues labelled Staff only

## Slide 32
Extra resources
Prusa
https://www.prusa3d.com/
https://blog.prusa3d.com/
Thingiverse
Checkout things other people have designed for 3D printing and save yourself a lot of time designing something someone else has successfully made. ​Remix / customise other people's designs.
https://www.thingiverse.com/categories
Functional Print
Check out the functional solutions people print up on Reddit.
https://www.reddit.com/r/functionalprint/

## Slide 33
THANKS FOR ATTENDING
Please complete our survey that will be sent out via Eventbrite.
Tag us on socials @statelibraryqld
Contact us on appliedcreativity@slq.qld.gov.au