## Slide 1: 3D Printing 101
Designing content for printing on The Edge 3D printers.

## Slide 2: Acknowledgement of Country We acknowledge Aboriginal and Torres Strait Islander peoples and their continuing connection to land and as custodians of stories for millennia. We respectfully acknowledge the land on which we all meet today, and pay our respects to elders past, present and emerging.

## Slide 3: WORKSHOP SUMMARY
In this workshop we will deep dive into the creation process for designing content for printing on The Edge 3D printers.
After attending this session, you should have a better understanding of prepping your 3D models printed at the best quality, most efficient speeds and much more.
Open Lab sessions are a chance to meet up with like-minded makers and tinkerers at The Edge with facilitators to support your creative needs in the space. Bookings are required to use the equipment and you will be able to book with your SLQ account once you have completed the relevant induction.
Wednesday 1.30pm – 8pm
Thursday 1.30pm – 8pm
Saturday 12pm – 5pm
For more info and to book, head to https://www.slq.qld.gov.au/visit/spaces/edge

## Slide 4: WORKSHOP SUMMARY
In this workshop we’ll break the session down into 5 sections where we look at the things you can do to get the most out of your 3Dprinting efforts at each stage of the 3D printing process.
We’ll work backwards in time starting by asking:

## Slide 5: WORKSHOP SUMMARY
In this workshop we’ll break the session down into 5 sections where we look at the things you can do to get the most out of your 3Dprinting efforts at each stage of the 3D printing process.
We’ll work backwards in time starting by asking:
how you are going to use the print?

## Slide 6: WORKSHOP SUMMARY
In this workshop we’ll break the session down into 5 sections where we look at the things you can do to get the most out of your 3Dprinting efforts at each stage of the 3D printing process.
We’ll work backwards in time starting by asking:
how you are going to use the print?
how much post print finishing and assembly?

## Slide 7: WORKSHOP SUMMARY
In this workshop we’ll break the session down into 5 sections where we look at the things you can do to get the most out of your 3Dprinting efforts at each stage of the 3D printing process.
We’ll work backwards in time starting by asking:
how you are going to use the print?
how much post print finishing and assembly?
What you can do to make sure the printer does the best job?

## Slide 8: WORKSHOP SUMMARY
In this workshop we’ll break the session down into 5 sections where we look at the things you can do to get the most out of your 3Dprinting efforts at each stage of the 3D printing process.
We’ll work backwards in time starting by asking:
how you are going to use the print?
how much post print finishing and assembly?
What you can do to make sure the printer does the best job?
What slicer settings you’ll use to meet your needs?

## Slide 9: WORKSHOP SUMMARY
In this workshop we’ll break the session down into 5 sections where we look at the things you can do to get the most out of your 3Dprinting efforts at each stage of the 3D printing process.
We’ll work backwards in time starting by asking:
how you are going to use the print?
how much post print finishing and assembly?
What you can do to make sure the printer does the best job?
What slicer settings you’ll use to meet your needs?
How you can design your parts to get the best possible 3D printing outcomes?

## Slide 10: But first What’s a reasonable thing to try and make on the 3D printers at The Edge?
Notes: What are Inherent limitations of FDM (Fused Deposition Modelling)
Even at highest available print resolution, fine detail on small objects competes with unavoidable texture that characterises the printing process
Limitations compounded if printing with filament other than PLA+

## Slide 11: Tinkercad refresher
Navigating space.
Combining shapes.
Imports and exports
Brief
Use tinkercad to quickly design a chess piece to hide a key.
You have 10 mins

## Slide 12: How are you going to use the print?
Notes: Is it decorative? is it part of some thing practical? Are you printing something to learn more about the process.
How good does it need to be? If its decorative how good does need to look, will FDM make the grade will you need to do some post printing work on it like sanding and priming?
If it’s a practical print how stong does it need to be? How pretty does int not need to be
whats the minimum viable product and what are you shooting for.

## Slide 13: 2. How much post print finishing and assembly do you want to do?

## Slide 14: 3. What you can do to make sure the printer does the best job?
Notes: Filament heater
clean bed
are you using the right filament
maybe you'd be better off casting instead of printing multiples

## Slide 15: 4. What slicer settings will you use?

## Slide 16: 4. Slicer settings
Repair holes open edges and inverted surfaces
Notes: https://fabconvert.com/file-repair/stl
https://products.aspose.app/3d/repairing/stl

## Slide 17: 4. Slicer settings
Orient object on print plate

## Slide 18: 4. Slicer settings
Sinking objects

## Slide 19: 4. Slicer settings
Perimeter count verses infill

## Slide 20: 4. Slicer settings
Types of supports

## Slide 21: 4. Slicer settings
Do you want a brim

## Slide 22: 4. Slicer settings
WARNING: detected print stability issuses: [More]

## Slide 23: 4. Slicer settings
Cutting models to eliminate or reduce supports

## Slide 24: 4. Slicer settings
Variable layer heights

## Slide 25: 5. Design for 3D printing
Fillets and Chamfers

## Slide 26: 5. Design for 3D printing
Design you object in parts for later assembly

## Slide 27: 5. Design for 3D printing
Locators

## Slide 28: 5. How you can design your parts to get the best possible 3D printing outcomes?

## Slide 29: More learning resources
PrusaSlicer | Prusa Knowledge Base (prusa3d.com)
tinkercad.com/skills/3d-printing
hubs.com/knowledge-base/design-for-3d-printing/
youtube.com/@MakersMuse
Wiki.slq.qld.gov.au
https://teachingtechyt.github.io//